## Slide 1: EPC-20-006 Group 1 Overview Development of Climate Projections for California and Identification of Priority Projections* A collaboration amongst SIO/UCSD, UCLA and UC Berkeley Sponsored by the California Energy Commission through the Electric Program Investment Charge (EPIC) program
*Now called General Use Projections

## Slide 2: Types of Downscaled Data
** Variables: Tmin, Tmax, precipitation, diurnal temperature range, RH min, RH max, surface downward shortwave, vector winds

## Slide 3: New, higher resolution training data uses WRF to interpolate between stations for more realistic precipitation

## Slide 4: New ensemble bias correction scheme better represents extreme precipitation events

## Slide 5: New hybrid downscaling scheme uses WRF-projected future weather patterns at the end of the century
New method limits the stationarity assumption

## Slide 6: More data available to address stakeholder needs
1. More variables to answer stakeholder questions
  LOCA 1: Tmin, Tmax, P, 10-meter windspeed, daily min and max of relative humidity; downward solar radiation
  LOCA 2: Tmin, Tmax, P, 10-meter windspeed; daily min and max of relative humidity; downward solar radiation, 10-meter U, V wind components (vector wind), specific humidity
2. More emissions scenarios to explore possible futures
  LOCA 1: 2 RCPs: 4.5, 8.5 (“medium-low” and “high”)
  LOCA 2: 3 SSPs: 245, 370, 585 (“medium-low”, “medium”, and “high”. Earth currently close to SSP 370)
3. More ensemble members available for stakeholders who need to evaluate natural variability
  LOCA 1: Only one ensemble member available
  LOCA 2: Up to 10 ensemble members (determined by what the original GCMs made available)
4. Potentially more hourly data available
  LOCA 1: Hourly temperature data at 32 stations
  LOCA 2: Hourly temperature data at 32 stations, potentially other variables and stations if stakeholders have access to observed data they can share with us for training the model

## Slide 7: Summary: LOCA version 2 improvements
Improved, higher resolution training data set
  New approach better depicts effects of California’s topography; 3 km vs. 6 km in version 1
Improved representation of precipitation extremes
  Critical for flooding and water management
Hybrid downscaling scheme
  More realistic projections for coming decades
  Limits stationarity assumption
More variables
  Supports a wider range of stakeholder applications
More runs, multiple ensemble members
  Allows better understanding of uncertainty, natural variability, and extremes
More emissions scenarios
  Better understanding of possible future human/societal/policy choices

## Slide 8: General Use Projections (previously known as “Priority Projections”)
What are General Use Projections?
  A subset of the 199 downscaled LOCA Hybrid GCM runs that are recommended to use in order to capture that range of projections
Why have General Use Projections?
  Using common projections between analyses support coordination, comparisons and collaboration across jurisdictional and other types of boundaries
Should I only use the General Use Projections?
  No, it is always better to use the full set of runs if you are able. Using the General Use Projections is the minimum number of projections that should be used in any analysis

## Slide 9: Deciding General Use Projections
Eligibility to be considered for General Use Projections
  Only considering model runs that have all the LOCA variables
    (e.g. dismiss model runs which didn’t save daily winds)
  Only considering models that have a SSP370 scenario
  Will try to include some WRF models
  Model skill is already included in the 15 model selection, but additional skill factors may be included
Selection of Metrics for General Use Projections
  Metrics have been pared down to a small number because too many uncorrelated metrics would average out the scores of the models, reducing the ability of the metrics to usefully distinguish between models.
  Need to ensure that metrics show a meaningful range
  Favor metrics that are simple variables, avoid those that are derivatives of several variables.
  Target SSP370 with a 2045-2074 mid-century period
  Every metric needs a weight to calculate the final combined model score

## Slide 10: General Use Projections Selection Metrics
Average summer daily max temperature (population weighted)
  Indicator of different types of heatwaves
P. Yao

## Slide 11: General Use Projections Selection Metrics, continued
Average summer daily max temperature (population weighted)
  Indicator of different types of heatwaves
~ P. Yao

## Slide 12: General Use Projections Selection Metrics, continued
Average summer daily max temperature (population weighted)
  Indicator of different types of heatwaves
Daily winter minimum temperature
  Captures trends for coolest part of the year & heating use

## Slide 13: General Use Projections Selection Metrics, continued
Average summer daily max temperature (population weighted)
  Indicator of different types of heatwaves
Daily winter minimum temperature
  Captures trends for coolest part of the year & heating use
Annually averaged precipitation volume
  Captures changes in the overall precipitation
Number of daily events exceeding 95th percentile
  Capture the frequency of extreme events which relates to all the wet metrics
* Need to assess range in the models. May change to changes in wind power in generation area.

## Slide 14: General Use Projections Selection Metrics, continued
Annually averaged precipitation volume
  Captures changes in the overall precipitation
Number of daily events exceeding 95th percentile
  Capture the frequency of extreme events which relates to all the wet metrics

## Slide 15: General Use Projections Selection Metrics, continued
Average summer daily max temperature (population weighted)
  Indicator of different types of heatwaves
Daily winter minimum temperature
  Captures trends for coolest part of the year & heating use
Annually averaged precipitation volume
  Captures changes in the overall precipitation
Number of daily events exceeding 95th percentile
  Capture the frequency of extreme events which relates to all the wet metrics
Dry Spell intensity (lowest total precipitation in 10-year period)
  Captures a balance of acute and extreme drought events
Combined frequency and intensity of downslope winds (Santa Ana & Diablo Winds)*
  Captures changes in high wind events that can be impactful to fire weather
* Need to assess range in the models. May change to changes in wind power in generation area.