## Slide 1: How Much Can Working at Home Reduce GHG Emissions?
Ysbrand van der Werf, Ph.D.
22 July 2020

## Slide 2: Introduction
During the COVID-19 lockdown many people have been working at home with more success than had been thought possible. Gasoline sales plummeted and consequently emissions from motor vehicles have also plummeted.
This leads one to ask: how much can increased work at home reduce GHG emissions?
The analysis presented here is an attempt to quantify the reduction in GHG emissions from feasible increases in working at home

## Slide 3: Data and Organization
Three types of data
1. Workforce: US census
2. Commuting: US census and CSTDM
3. Emissions: EMFAC
They are used to show us
A. the pre-COVID reduction in GHG emissions from working at home
B. three scenarios of possible GHG reductions that would result from an increase in working at home

## Slide 4: California Workforce Data
Using county-level census data for 2018, which is the most recent available
From the American Community Survey
This data includes exactly 30 counties that include over 96% of workforce.

## Slide 5: California Commuter Data
The American Community Survey provides data on commute mode by sector for each county—13 sectors and 5 modes.
The modes are:
  Drive alone—75 percent
  Carpool or vanpool—10 percent
  Public Transit—5 percent
  Miscellaneous—5 percent
  Work at Home—5 percent
Of these, we assume that only those who drive alone can reduce GHG emissions

## Slide 6: California Commuter Data, pt. 2
Two sectors are used for this analysis:
“Information and finance and insurance, and real estate and rental and leasing”
“Professional, scientific, and management, and administrative and waste management services”
Combined, these account for:
22 percent of California’s workforce
41 percent of California’s work-at-home force

## Slide 7: California Commuter Data, pt. 3
ACS provides data for commute time in each county, but not for commute distance
Data for commute distance in each county for 2015 is from CSTDM data for the California Transportation Plan 2040
This 2015 commute distance correlates well with 2018 commute time (it actually correlates better than 2015 commute time).
I assume that this is the same for all sectors

## Slide 8: California Emissions Data
Emission data by vehicle class are from EMFAC estimates for 2018 by CARB
EMFAC emissions per mile and trip are both used
Vehicle population by class are taken from DMV data prepared by Energy Commission staff and are mapped to the EMFAC classes
97% of vehicles are fueled by gasoline, but all are assumed to be gasoline fueled for this study

## Slide 9: In Summation
Data analyzed is for
Gasoline—97%
Thirty counties—96%
Single drivers only—75%
Two economic sectors—22%
Of the 17,418,097 commuters in California, we look at 2,770,659 commuters who can reduce their GHG emissions by working at home.

## Slide 10: How Much Are GHG Emissions Reduced?
GHG Emissions by Single Drivers and Avoided Emissions (metric tons CO2e per day) |  |  |  |  | 
 | A Pre-COVID emissions |  | B Pre-COVID emissions avoided from work at home |  | B
 |  |  |  |  | (A+B)
Statewide | 115,810 |  | 7,262 |  | 6%
Two selected sectors | 23,973 |  | 2,962 |  | 11%
State employees | 3,897 |  | 262 |  | 6%
in Sacramento | 474 |  | 14 |  | 3%

## Slide 11: How Much Could They Be Reduced?
Reduction in GHG Emissions from Single Drivers Working at Home (metric tons CO2e per day) |  |  |  |  |  |  |  | 
 | B Pre-COVID avoided emissions |  | C One-day-per-week scenario |  | D Three days per week |  | E Five days per week | 
Statewide | 7,262 |  | 4,795 |  | 14,384 |  | 23,973 | 
Two selected sectors | 2,962 |  | 4,795 |  | 14,384 |  | 23,973 | 
State employees | 262 |  | 779 |  | 2,338 |  | 3,897 | 
in Sacramento | 14 |  | 95 |  | 285 |  | 474 | 

## Slide 12: How Much More Can the Reduction Be?
Pre-COVID, 6% of statewide commuting GHG emissions are avoided through work at home
If just two sectors of the workforce worked at home this could be increased:
once a week 10%
3 times a week 18%
5 days a week 25%
Chart: Possible Statewide Emission Reductions (metric tons CO2e daily)
| Pre-COVID (B) | Plus 1 day/week (B + C) | Plus 3 days/week (B + D) | Plus 5 days/week (B + E)
Reductions | 7262.2818 | 12056.8996 | 21646.1353 | 31235.3709
Emissions | 115810.2959 | 111015.678 | 101426.4424 | 91837.2067

## Slide 13: Annual Total Passenger Vehicle Emissions
GHG Emissions and GHG Reductions by Single Drivers in Two Sectors |  |  |  |  | 
 | Vehicles or individuals | Gallons of gasoline | Million metric tons CO2e per year |  | 
All passenger vehicles | 26.9 million | 14.5 billion | 140 |  | 100%
Vehicles of single commuters | 13.7 million | 3.0 billion | 29 |  | 21%
Two sectors, passenger vehicles commuting (A) | 2.8 million | 625.0 million | 6.0 |  | 4.3%
Avoided during pre-COVID commute (B) | 454,034 | 77.2 million | 0.7 |  | 0.5%
Total reduction, 1 day/week (B + C) |  | 202.2 million | 1.9 |  | 1.4%
Total reduction, 3 days/week (B + D) |  | 452.2 million | 4.3 |  | 3.1%
Total reduction, 5 days/week (B + E) |  | 702.2 million | 6.7 |  | 4.8%
Source: “All passenger vehicles” from CARB EMFAC data; others from CEC analysis

## Slide 14: Conclusion
This analysis examined a subset of commuters in order to get an idea of how much reduction in GHG emissions could be obtained by telecommuting and showed that it offers opportunities for substantial reduction in GHG emissions at minimal cost.
Possible improvements
Explore better alignment between EMFAC and census data
Sector data might be improved upon
Expand to include carpools and mass transit for examining scenarios with many working at home
(include other fuels and counties)

## Slide 15: Thank You!