## Slide 1: Price Discussion
Jul 15, 2021
Michael (Misho) Penev
National Renewable Energy Laboratory
Demand Analysis Working Group (DAWG) Meeting: California Transportation Energy Demand Forecast Inputs and Assumptions

## Slide 2: National Light-Duty FCEV Supply Chain: Overview
Energy prices (natural gas, electricity, etc.)
Renewables (biomass, solar, wind)
Terrain, rights of way, etc.
The SERA model simulates least-cost hydrogen infrastructure supply systems for urban FCEV markets
Energy Resources
Hydrogen Production
Storage & Delivery
Retail Station Networks
Los Angeles
Central and onsite production facilities
Capacity sized to meet forecasted demand
Economies of scale balanced with delivery costs
Truck delivery, rail, and pipeline.
Cost is sensitive to volume, distance
Seasonal and weekly storage
Networked supply to multiple cities
Coverage stations for FCEV introductions
Station sizes increase with market growth
Liquid and pipeline delivery networks compete for large stations
https://www.nrel.gov/hydrogen/sera-model.html

## Slide 3: FCEV Supply Chain: SERA optimizes production, transmission, delivery and dispensing
Note:
GH2: Gaseous H2
LH2: Liquid H2
Inputs: Resource prices, technology cost and resource data, FCEV demand
Optimization: SERA finds least-cost infrastructure to meet demand, technology, and resource constraints
Outputs: “blueprints” for hydrogen supply chain (production, transmission, delivery, dispensing)
(Above) Example supply chain pathways for SERA to select from
(Right) Visualization of optimized light-duty vehicle hydrogen supply chain in 2050

## Slide 4: 2020 Hydrogen Price Projection
Analysis basis:
National analysis informs learning curves
CA analysis applies specific scenarios (% renewables, vehicle sale projections, existing stations)
Historic price informs near-term trajectory (no competitive market forces)
SERA computes future profited costs by scenario (assumes competitive market)
Transition between current and future price curves based on interpolation

## Slide 5: Historic H2 Price Based on Reporting Agreements
Price entails pre-paid valuation of fuel included in first 3-year lease agreements
Drivers’ choice of fueling location is only based on convenience
Stations offering lower price fuel do not benefit from higher volume sales
Lower priced stations yield lower revenues
https://www.nrel.gov/hydrogen/assets/images/cdp-retail-infr-89.jpg

## Slide 6: H2FAST Framework For Retail Station Analysis
The Hydrogen Financial Analysis Scenario Tool (H2FAST)
  Generally accepted accounting principles (GAAP) analysis of individual hydrogen infrastructure projects (production, distribution, retail)
  Annual computation of income statements, cash flow statements, balance sheets.
  Cost attribution by category
  Incentive policy analysis
  Risk analysis
Operating costs
Capital costs
Incentives impact
Incentives
Financing
Financial performance
Scenarios
Risk analysis
Cost attribution
Incentives
scenarios
Risk analysis
https://www.nrel.gov/hydrogen/h2fast.html

## Slide 7: Single Station Cash Flow Analysis H2FAST
600 kg/d station
(before 2021 update)
1,600 kg/d LH2 station
(latest update)
Base case financial performance analysis of hydrogen stations in a CA costs and incentive environment assume 8% nominal ROE (competitive market assumption)

## Slide 8: Competitive Consideration: Clustering vs. Coverage
https://www.reddit.com/r/mildlyinteresting/comments/aezmhd/lowes_and_home_depot_right_next_to_each_other/
https://www.planetizen.com/node/65765
Hotelling's law
Attract customers based on cost & product differentiation by clustering with competitor
Minimize customer choice around product and price and not convenience of location
Evenly split market if prices and quality are identical
Other benefits
Realize sales volume vs. price differential
Redeem brand loyalty
Monetize market preference for product differentiation e.g. renewable content of H2
Hardware stores
Gas stations
Fast Food
H2 infrastructure emphacises coverage.
Competitive markets emphacise clustering.

## Slide 9: Station Coverage Status Bird’s Eye View (Including planned stations)

## Slide 10: Distance to Nearest Fueling Alternative
Linear distance among any stations (miles)
Includes planned stations
Average station-station distance = 4.7 miles
Excludes connectors
(Santa Barbara, Truckee, Harris Ranch)
Linear distance to nearest alternative operator station (miles)
Includes planned stations
Average distance between alternative fueling retailers = 6.7 miles
Coverage perspective
Competitive perspective

## Slide 11: Monetization of Break-Even Savings to Alternate Station ($/kg)
B $/kg
A $/kg
B = Savings?
Simple method (full round-trip cost):
Based on fuel used for round-trip & time value of the driver
Ave drive speed = 30mph
Detour factor = 1.4 (linear -> on-road distance)
Time value = $10/h
Fuel economy = 60mpg
Fuel cost= $16/kg
Refuel quantity = 3kg
Example: 1 mile distance to alternative:
round-trip cost =
0.09h * $10/h
+ 2.8mile * $16/kg / 60 mpkg = $0.93 time val + $0.75 fuel
  min savings per kg = ($0.93+.75)/3kg = $0.56/kg

## Slide 12: Distribution of Break-Even Savings ($/kg)
Average break even price differential = $3.8 /kg
B $/kg
A $/kg
I’ll fuel at B for >$3.8/kg savings
I’ll fuel at B for $0/kg savings
I’ll fuel at B for >$1.9/kg savings
On average, suppliers need to offer ~$1.9/kg savings to have significant impact on sales volume
Shorter distance to alternative suppliers reduces savings requirement
Halfway
point

## Slide 13: Retail Station Cost Dimensions With Incentives
Baseline scenario:
Delivered H2 = $7/kg
HRI credit = $2.3/kg
LCFS credit = $2.3/kg
Capital grant = $1.45M
Station life = 20 yrs
Long term utilization = 80%
Utilization growth = 5 yrs
Total station cap = $1,400/kg-day
Vertically integrated suppliers can look for efficiencies in full supply chain.
Extending station life, reducing capital and operating costs are desirable attributes for more competitive performance.
Baseline external parameters
Baseline retailer specific parameters

## Slide 14: Retail Station Cost Dimensions Without Incentives (Risk Averse View)
Baseline scenario:
Delivered H2 = $7/kg
HRI credit = $0.0/kg
LCFS credit = $0.0/kg
Capital grant = $0.0M
Station life = 20 10 yrs
Long term utilization = 80%
Utilization growth = 5 yrs
Total station cap = $1,400/kg-day
Baseline external parameters
Baseline retailer specific parameters

## Slide 15: Price Downward Pressure Discussion
Driver out-of-pocket contribution is essential
enables market price response
consumer cost % too low: price-sales response too low
consumer cost % too high: reduces FCEV adoption rate
realistic price improves market optics and improves consumer planning on future expense profile
Station clustering vs. station coverage impact
short distance between suppliers magnifies sales volume impact of price differentials
availability of H2 from multiple suppliers at a location improves resilience from supply disruptions and demand spikes
clustering enhances brand loyalty & product differentiation effect: e.g. % renewables content
Station placement for coverage
Station placement for clustering
price competitiveness