## Slide 1: DEMAND ANALYSIS WORKING GROUP (DAWG)
AAEE & AAFS
Scenario Development & Deployment
September 15, 2021 11-11:30am
Ingrid Neumann, Ph.D.
CEC - EAD

## Slide 2: Additional Achievable Energy Efficiency (AAEE)

## Slide 3: Single Managed Forecast Set
“Energy Commission, in consultation with the CPUC and the CAISO, considered public input in selecting a single or managed demand forecast from the adopted forecast report for use in transmission planning and procurement. This set of forecast numbers is a combination of two forecast components: a base case with weather variants and an additional achievable energy efficiency (AAEE) scenario. Combined together, these create the single or managed forecast.”
Three baseline cases and five scenarios of AAEE
The mid-AAEE forecast scenario will be used for system-wide and flexibility studies relied upon for procurement and transmission planning purposes.
Because of the local nature of reliability needs and the difficulty of forecasting locally disaggregated AAEE, the low-mid-AAEE scenario will be used for local studies.

## Slide 4: Proposed 2021 AAEE
For 2021 we will be using the same saving accounting, aggregation, and extrapolation methodology & tools as were developed for 2019 with the addition of some new capabilities
  Hourly GHG savings from gas and electric EE
  Extrapolation of potential savings out to 2050
Historical data and potential savings projections are being updated
Some beyond utility workbooks are being removed while others are being added or enhanced based on recent programmatic activities
Notes: Energy Efficiency (EE) tracking and projection/forecast scenarios
Incorporate new data such as from utility and other incentive programs to update historical savings as improve projections
Add new EE programs savings projections
Incorporate updates to code and standards in savings projections
Consider overlap in customer segments being targeted by different programs
Consider market-based activities that may result in EE savings that are not being captured elsewhere

## Slide 5: Additional Achievable Energy Efficiency (AAEE) 2021 Process Flow Overview
2021 CMUA PG Study
POU Projections
2021 CPUC PG Study
IOU Projections
CEC Beyond Utility Programs tool allows scenario design for Beyond Utility AAEE first year Projections 2022-2035
Scenario Design
POU AAEE first year
Projections 2022-2041
Scenario Design
IOU AAEE first year
Projections 2022-2032
Data Integration Tool for
Total Cumulative AAEE Projections by year 2022-2035
by utility, sector, end use & scenario
AAEE Hourly Tool
Total 8760 Hourly AAEE Projections by year 2022-2035
by utility, sector, end use & scenario
AAEE
C&S
Notes:   consider what is the appropriate way of extended PG Study impacts from 2033-2035?
  linear maybe ok since short time frame… consider trend for 2021 ACC which is upwards so maybe linear is actually appropriate since extending longer would increase savings; would also be consistent with IRP (done with bundles ~ sector/end-use)

## Slide 6: Scenario Development for 2021 AAEE
IOU Potential Program Savings
Codes and Standards Savings
POU Potential Program Savings
Beyond Utility Program Savings

## Slide 7: Proposed 2021 IOU AAEE Scenario Design
Notes: anything lower drops PGE portfolio below 1.0 in the first few years
M&O is increased parameter in the bass diffusion model regarding marketing effectiveness for rebate programs.
program engagement is increased BROs Programs participation

## Slide 8: Proposed 2021 IOU component of AAEE mid-mid Sc3 BAU
Notes: anything lower drops PGE portfolio below 1.0 in the first few years
M&O is increased parameter in the bass diffusion model regarding marketing effectiveness for rebate programs.
program engagement is increased BROs Programs participation

## Slide 9: Reference Demand Scenario IOU component of AAEE mid-mid Sc3 BAU
Based on reference TRC Scenario of the CPUC’s 2021 Potential and Goals Study
This is the scenario tapped in the proposed decision from August 20 which will be voted on for the goals September 23
Uses the 2020 ACC for 2022-2023 and 2021 ACC for 2024-2032
LI sector savings projections based on ESA decision goals already adopted for 2022-2026
extrapolate from 2033 to 2050
  Use trend forecast based on last three years of data provided; by sector end-use
  Except for LI, held those savings constant from last year (2032)
Notes:   consider what is the appropriate way of extended PG Study impacts from 2033-2035?
  linear maybe ok since short time frame… consider trend for 2021 ACC which is upwards so maybe linear is actually appropriate since extending longer would increase savings; would also be consistent with IRP (done with bundles ~ sector/end-use)

## Slide 10: Proposed 2021 POU AAEE Scenario Design
For each of the 38 California POUs, energy efficiency savings projections were defined for the years 2022 to 2041 by GDS Associates on behalf of the CMUA
Savings were characterized by sector, by end use, and by program name
  Behavorial Programs were named
  Fuel Substitution impacts were not included
first-year Cumulative Market Potential was used as the reference level
to create POU potential scenarios, the team calculated sector-by-sector (Residential, Commercial, Industrial, and Agricultural) ratios from the 2021 PG study IOU data
Notes: In order to create POU potential scenarios, the team calculated sector-by-sector (Residential, Commercial, Industrial, and Agricultural) ratios from the 2021 PG study IOU data. This was done by summing total sector savings among each of the defined IOU scenarios. For example, if the IOU data indicated that the conservative scenario for the commercial sector resulted in 7.5% fewer savings than the reference case, that same ratio was applied to derive a POU conservative case from the existing POU reference data.

## Slide 11: Reference Demand Scenario POU component of AAEE mid-mid Sc3 BAU
For each of the 38 California POUs, energy efficiency savings projections were defined for the years 2022 to 2041 by GDS Associates on behalf of the CMUA
extrapolate from 2042 to 2050
  Use trend forecast based on last three years of data provided; by sector end-use
Reference Demand Scenario POU component of AAEE mid-mid Sc3 BAU
Notes: In order to create POU potential scenarios, the team calculated sector-by-sector (Residential, Commercial, Industrial, and Agricultural) ratios from the 2021 PG study IOU data. This was done by summing total sector savings among each of the defined IOU scenarios. For example, if the IOU data indicated that the conservative scenario for the commercial sector resulted in 7.5% fewer savings than the reference case, that same ratio was applied to derive a POU conservative case from the existing POU reference data.

## Slide 12: Proposed 2021 C&S AAEE Scenario Design
Notes: probably everything "on the books" will be included in the baseline forecast
2022 T24 will be included in AA's because of FS component

## Slide 13: Reference Demand Scenario C&S component of AAEE mid-mid Sc3 BAU
Reference Demand Scenario C&S component of AAEE mid-mid Sc3 BAU
extrapolate from 2033 to 2050
  First year T24 EE savings through 2030 (no new EE expected from T24 after 2028 vintage)
  T20 first year savings estimated through 2036 in reference case (2038 for more aggressive scenarios)
  Fed App first year savings estimated through 2038 in reference case
Almost everything "on the books" will be included in the baseline forecast
2022 T24 will be included in AA's because of FS component
Notes: probably everything "on the books" will be included in the baseline forecast
2022 T24 will be included in AA's because of FS component

## Slide 14: Proposed 2021 Beyond Utility AAEE Scenario Design
Notes: established programs with historical performance data and expected future funding allocations
limited historical data on a pilot or other subset of programs and reasoned assumption on future funding allocations
assumptions based on pilot or proposed programs
limited assumptions based on pilot or proposed programs
CVR: using data from literature review from PGE, SCE, SMUD as well as recent update from contact at Glendale
Ind/Ag: calculate achievable savings without mechanism to realize programs minus existing programs then X amount of years to attain achievable
savings
AQMD: to achieve air quality attainment south coast programs, maybe more in future as point of sale restriction on appliances

## Slide 15: Reference Demand Scenario BU component of AAEE mid-mid Sc3 BAU
Reference Demand Scenario BU component of AAEE mid-mid Sc3 BAU
programs with historical performance data and expected future funding allocations will be included
savings estimates from programs requiring more assumptions because historical data is only based on pilot programs or of proposed programs will be included at a more conservative level
extrapolate from 2033 to 2050
  Some programs end so not extrapolated
  Others held constant at last projected year, few trended out
Notes: probably everything "on the books" will be included in the baseline forecast
2022 T24 will be included in AA's because of FS component

## Slide 16: Additional Achievable Fuel Substitution (AAFS)

## Slide 17: What work has EAD done on FS?
Developed “what-if” Fuel Substitution Scenario Analysis Tool (FSSAT)
  Used the FSSAT to analyze building electrification scenarios in our AB 3232 Analysis described in the recently published California Building Decarbonization Assessment
Each of the electrification scenarios meeting or exceeding the AB3232 target have substantial incremental electric energy added due to electrification efforts
  In addition to increasing peak loads electrification can shift the dates and times of these peaks; winter loads are affected more than summer loads
AB 3232 analysis based on “what if”; can’t use AB 3232 scenarios as a starting point for AAFS
We are currently completing work with GH on incorporating more program-oriented inputs in our improved EE/FS analysis tools for use in the 2021 IEPR

## Slide 18: Modeling electrification: Fuel Substitution Scenario Analysis Tool (FSSAT) main processes flow chart
Notes: BAU mid-mid gas forecast
Electric for Gas technology substitution
Annual and hourly outputs for incremental electricity added and GHG emissions

## Slide 19: Use AAEE as a template for AAFS
For 2021 we are developing Additional Achievable Fuel Substitution (AAFS) as an hourly load modifier to the baseline demand forecast.
AAFS is conceptualized as separate from AAEE
DAWG stakeholder workshop June 23 “AB 3232 and Fuel Substitution”
IEPR Commissioner Workshop August 5 Electricity & Natural Gas Demand Forecast: Inputs & Assumptions
DAWG stakeholder workshop September 9 “AAEE & AAFS Preliminary Scenario Designs”

## Slide 20: Scenario Development for 2021 AAFS
IOU Potential Program Savings
Codes and Standards Savings
POU Potential Program Savings
Beyond Utility Program Savings

## Slide 21: Proposed 2021 IOU AAFS Scenario Design
Notes: PG Study did not include any LI FS
Because only SCE currently included FS measures in their low income programs, Guidehouse used SCE data as a baseline to extrapolate total program savings forecasts for the years 2022 and beyond. For the years 2022-2023, Guidehouse assumed that only SCE would have FS savings, but with a reasonable timeline assumption PG&E and SDG&E would start having savings in 2024 and then continue along with SCE until ending FS savings in 2035. The team assumed that FS would continue until 2035, and would have zero savings after that year, as all potential fuel substitution may have happened by then or applicable codes and standards will apply.
Water Heating Heat Pump, Water Heater Space Heating Central HP, Space Heating Mini Split HP, Appliance HP Clothes Dryer Appliance, Inductive Range

## Slide 22: Proposed 2021 IOU component of AAFS mid-mid Sc3 BAU
Notes: PG Study did not include any LI FS
Because only SCE currently included FS measures in their low income programs, Guidehouse used SCE data as a baseline to extrapolate total program savings forecasts for the years 2022 and beyond. For the years 2022-2023, Guidehouse assumed that only SCE would have FS savings, but with a reasonable timeline assumption PG&E and SDG&E would start having savings in 2024 and then continue along with SCE until ending FS savings in 2035. The team assumed that FS would continue until 2035, and would have zero savings after that year, as all potential fuel substitution may have happened by then or applicable codes and standards will apply.
Water Heating Heat Pump, Water Heater Space Heating Central HP, Space Heating Mini Split HP, Appliance HP Clothes Dryer Appliance, Inductive Range

## Slide 23: Reference Demand Scenario IOU component of AAFS mid-mid Sc3 BAU
Based on reference TRC Scenario of the CPUC’s 2021 Potential and Goals Study
This is the scenario tapped in the proposed decision from August 20 which will be voted on for the goals September 23
Uses the 2020 ACC for 2022-2023 and 2021 ACC for 2024-2032
No LI sector savings projections included so they were modeled after the recent ESA filing from SCE and scaled to all IOU’s
extrapolate from 2033 to 2050
  Use trend forecast based on last three years of data provided; by sector end-use
  Except for LI, held those savings constant from last year (2032)
Notes:   consider what is the appropriate way of extended PG Study impacts from 2033-2035?
  linear maybe ok since short time frame… consider trend for 2021 ACC which is upwards so maybe linear is actually appropriate since extending longer would increase savings; would also be consistent with IRP (done with bundles ~ sector/end-use)

## Slide 24: Proposed 2021 POU AAFS Scenario Design
Interviewed all willing POU’s…
Relied on preliminary pilot program data from LADWP projected for 2021-2052 and data from SMUD, Pasadena, Palo Alto on reasoned cost projections, number of participant projections, or estimated future GHG reductions
assigned a fuel substitution delay or ‘head start’ to each POU, relative to the LADWP fuel substitution timeline. SMUD, for example, was judged to be two years ahead of LADWP in fuel substitution implementation, while most other POUs were judged to be two years behind LADWP
Notes: POU FS LADWP data and SMUD, Pasadena, Palo Alto etc. interviews
(To extrapolate the data to POUs across the entire state, Guidehouse first used the GDS Associates POU energy savings projections data to determine the relative size of each POU’s total energy savings potential, relative to LADWP. The projected savings for each POU was summed for the five years from 2022 to 2026 and compared to create a ‘savings potential multiplier’. Next, Guidehouse assigned a fuel substitution delay or ‘head start’ to each POU, relative to the LADWP fuel substitution timeline. SMUD, for example, was judged to be two years ahead of LADWP in fuel substitution implementation, while most other POUs were judged to be two years behind LADWP.)
The team analyzed the percent difference between conservative, reference, and aggressive scenarios outlined in the IOU PG study data to calculate an average ‘scenario factor’ between the conservative and reference case (as well as a separate scenario factor for the difference between the aggressive and reference case). Factors were calculated based on IOU Fuel Substitution programs combined. Although the PG study data reveals slight differences in the ratios from year to year with small variations, the team used a simplified average from 2021 to 2031 for the analysis.

## Slide 25: Reference Demand Scenario POU component of AAFS mid-mid Sc3 BAU
Relied on preliminary pilot program data from LADWP projected for 2021-2052 and data from SMUD, Pasadena, Palo Alto on reasoned cost projections, number of participant projections, or estimated future GHG reductions
No need for additional extrapolation
Reference Demand Scenario POU component of AAFS mid-mid Sc3 BAU
Notes: In order to create POU potential scenarios, the team calculated sector-by-sector (Residential, Commercial, Industrial, and Agricultural) ratios from the 2021 PG study IOU data. This was done by summing total sector savings among each of the defined IOU scenarios. For example, if the IOU data indicated that the conservative scenario for the commercial sector resulted in 7.5% fewer savings than the reference case, that same ratio was applied to derive a POU conservative case from the existing POU reference data.

## Slide 26: Proposed 2021 C&S AAFS Scenario Design
In accordance with the CPUC’s 2020 and 2030 zero-net-energy goals, we originally considered the zero-net-energy requirements for residential and nonresidential buildings for the 2019 and 2028 standards, respectively.
Since then, the state began focusing on decarbonization, the CEC implemented changes for the 2022 Title 24 standards to include a GHG metric. To this end two new workbooks were created: Nonres/Com New Construction Fuel Sub and Residential Fuel Sub, Residential A&A was modified to have an EE path and a FS path with an uptake percentage for each adding to 100%

## Slide 27: Reference Demand Scenario C&S component of AAFS mid-mid Sc3 BAU
Reference Demand Scenario C&S component of AAFS mid-mid Sc3 BAU
2022 T24 will be included in AA's because of FS component
electric space OR water heating NC & AA for Residential
Some prescriptive baseline requirements for Nonresidential NC
extrapolate from 2033 to 2050
  First year T24 FS savings through 2030 (no new EE expected from T24 after 2028 vintage; unclear if additional electrification would be possible via T24)
Notes: probably everything "on the books" will be included in the baseline forecast
2022 T24 will be included in AA's because of FS component

## Slide 28: Proposed 2021 Beyond Utility AAFS Scenario Design
  we can add speculative “what if” technology-based FS to show what additional types of programmatic efforts may be necessary to reach these goals
  Programmatic FS may not be of the magnitude needed to meet various policy goals
  Programmatic FS can be input to the FSSAT to determine what remaining gas displacement remains
Notes: limited historical data on a pilot or other subset of programs and reasoned assumption on future funding allocations
assumptions based on pilot or proposed programs

## Slide 29: Reference Demand Scenario BU component of AAFS mid-mid Sc3 BAU
Reference Demand Scenario BU component of AAFS mid-mid Sc3 BAU
Projections based on limited historical data on a pilot or other subset of programs and reasoned assumption on future funding allocations will be included at a reference level
impact estimates from programs assumptions based on pilot programs without historical data or proposed programs will be included at a more conservative level
extrapolate from 2033 to 2050
  Some programs end so not extrapolated
  Others held constant at last projected year, few trended out
Notes: probably everything "on the books" will be included in the baseline forecast
2022 T24 will be included in AA's because of FS component

## Slide 30: Consideration of which AAFS & AAEE Scenario’s are compatible
Need to consider which combinations of AAEE and AAFS scenarios are compatible with each other given total gas displacement potential and program funding sources.
Important when proposing inputs to the Policy/Compliance – High Electrification & Mitigation – High Electrification Scenarios
Notes:   Currently choose the AAEE Scenario first and give the baseline gas consumption forecast a “haircut” as part of designing an FSSAT scenario FS is only allowed for the remaining gas consumption after AAEE reduction.
    Pro: aligned with loading order
    Con: “low hanging fruit” may be better suited for FS than gas EE
    consider approaching this by designing gas AAEE and electric AAEE scenarios separately…?
    If the total FS MM Therms savings for a particular Gas Utility and Sector exceeds this specified threshold in a given year, then the gas savings for that Gas Utility and Sector will be scaled proportionally downward in that year. For example, if the threshold is set at 15% and PG&E residential FS gas savings is 20% of PG&E residential IEPR demand in a given year, then all residential PG&E gas savings for that year will be scaled down to 80% (1 - 0.2 = 0.8) of unadjusted savings.

## Slide 31: Policy/Compliance – High Electrification Demand Scenario
Policy/Compliance –
High Electrification Demand Scenario
Notes: probably everything "on the books" will be included in the baseline forecast
2022 T24 will be included in AA's because of FS component

## Slide 32: Mitigation – High Electrification Demand Scenario
Mitigation –
High Electrification Demand Scenario
Notes: probably everything "on the books" will be included in the baseline forecast
2022 T24 will be included in AA's because of FS component

## Slide 33: Thank you!
Ingrid.Neumann@energy.ca.gov