## Slide 1: Current Climate Change Analysis Practices in DWR’s using the Latest Climate Change Projections and a Weather Generator
Romain Maendly
Climate Action Coordinator
CA DWR / Executive Division
May 17th, 2024
C-DAWG

## Slide 2: Presentation Outline
1. Motivation
  Why combine a stochastic weather generator and downscaled General Circulation Models directly?
Weather-Regime Based Stochastic Weather Generator
Basic description of the weather generator
Scenario Generation
Demonstration of climate change scenarios generation with the Stochastic Weather Generator model
Latest Use Case
Draft – State Water Project Delivery Capability Report 2023

## Slide 3: 1. Motivation

## Slide 4: Why combine a stochastic weather generator and downscaled General Circulation Models directly?
Notes: Top-down approaches generally result in scenarios of future conditions that are easy to explain and can provide a range of impacts that explore possible outcomes. But, these scenarios, by themselves, are difficult to place in a probabilistic context and are generally not informed by specific factors that drive system risk or vulnerability. They are also highly sensitive to decisions about which climate models are included and cannot easily explore sensitivity to model selection.

## Slide 5: Planning Water Systems for Future Climate Conditions
Realized Hydroclimate:
+
Noise
(Natural variability)
Magnitude, frequency, timing, and sequencing of droughts and floods
Long-term, quasi- or aperiodic dry periods and pluvials
Space-time distribution of precipitation and temperature across a heterogeneous landscape
Signal
(Climate change trends)
Shifting snow accumulation / melt dynamics, rain-on-snow
Higher ET and soil moisture loss
Intensification of extreme precipitation
Shifts in location and frequency of storm tracks

## Slide 6: 2. Weather-Regime Based Stochastic Weather Generator

## Slide 7: Weather Regime Based Stochastic Weather Generation
Weather Regime - Mid‐latitude atmospheric intra‐seasonal variability is characterized by large‐scale flow patterns (“weather regimes”)
  Organize mid‐latitude storms
  Appear repeatedly at fixed geographical locations
  Persist beyond the lifetime of individual synoptic‐scale storms (days-weeks)
  Exhibit rapid transitions associated with nonlinear atmospheric dynamics
  Respond to external forcings (e.g., ENSO or anthropogenic effects)

## Slide 8: Weather Regimes
Notes: Ridiculously Resilient Ridge or persistent anticyclone
https://www.kqed.org/science/26293/ridiculous-ridge-may-be-back-to-prolong-california-drought

## Slide 9: 3. Scenario Generation

## Slide 10: Process-Based Understanding of Climate Change
Shifting snow accumulation / melt dynamics, rain-on-snow
Higher ET and soil moisture loss
Intensification of extreme precipitation
Shifts in location of storm tracks
More frequent storm events
Shift in the frequency, duration, or transition probabilities of weather regimes
Changes in the dynamics of ENSO
Thermodynamic VS. Dynamic

## Slide 11: Thermodynamic Precipitation-Temperature Scaling

## Slide 12: Climatic Scenarios

## Slide 13: Weather Regimes Support California-Wide Model Development and Deployment
Perturbed Historical Time series (1915-2018)
  Inputs: Livneh Untrimmed Precipitation & Livneh Detrended (1991-2020) Temperature
  Outputs: 23 Scenarios based on the historical period (Tmin, Tmax and Precip) with extreme precipitation scaling of 7% per °C.
WGEN Thermodynamic Time Series Only
  Inputs: Same as above, trained on the historical period (1948-2018)
  Outputs:
  1,000year daily weather-generated data (Tmin, Tmax and Precip)
  23 scenarios with extreme precipitation scaling of 7% per °C, +6 scenarios for sensitivity analysis

## Slide 14: 4. Latest Use Case

## Slide 15: Bottom-Up Climate Vulnerability Analysis with a Stochastic Weather Generator

## Slide 16: Bottom-Up Climate Vulnerability Analysis with a Stochastic Weather Generator (2)

## Slide 17: State Water Project (SWP) Delivery Capability Report
Bi-annual report of Existing and Future delivery capability
Key Planning Information for SWP water users (UWMP, IRWM, SGMP, AWMP, etc.)
Serve as the default climate change scenario for SWP planning (future energy resource, asset maintenance and management studies, EIR, etc.)
Notes: Over a range of hydrologic conditions
  Historic extended dry cycle
  Long-term average

## Slide 18: Link Stress Test and Climate Space and Assess Risk

## Slide 19: Model/Data Availability and Resources
DWR Climate Change Program Website: Resources for Water Managers
  https://water.ca.gov/Programs/All-Programs/Climate-Change-Program/Resources-for-Water-Managers
    Final Report
    California Natural Resources Agency Data Library: https://data.cnra.ca.gov/dataset/ca-weather-generator-gridded-climate-pr-tmin-tmax-2023
Weather Generator Tool Public Seminar
  YouTube Channel: https://www.youtube.com/watch?v=QQZ1MIoC2_0

## Slide 20: Introduction to Ca Water Plan Update 2021
Thank you!
Romain.Maendly@water.ca.gov