## Slide 1: Demand Analysis Working Group Tailpipe and Grid Emissions Calculations
Heidi Javanbakht
July 22, 2020

## Slide 2: Background
*CARB 2019 Edition, California GHG Emission Inventory: 2000-2017, page 6
CEC vision: “the Energy Commission is committed to reducing energy costs, curtailing greenhouse gas emissions, and ensuring a safe, resilient, and reliable supply of energy”
  Transportation is 40.1% of overall GHG emissions in the state*
SB 100: Requires that zero-carbon resources supply 100% of electric retail sales to end-use customers by 2045
  Future work will include demand scenarios evaluating the impacts of various strategies on transportation energy demand and GHG emissions

## Slide 3: Overview of Methodology
Tailpipe Emissions: Emission factors from CARB’s EMFAC are applied to the CEC’s vehicle stock and VMT
Grid Emissions from Charging PEVs: Emission factors determined by the CEC’s Supply Analysis Office are applied to the forecasted hourly electricity consumption

## Slide 4: Tailpipe Emissions
Annual Emissions =
Vehicle Stock x ((RUNEX x VMT)+(STREX x Trips)+(IDLEX x Oper_Days))
We will include the off-model adjustment factors for gasoline LDVs (CARB published guidance in response to the SAFE Vehicle Rule)
Challenges
  CEC vehicle classifications differ from EMFAC vehicle classifications
  CEC does not calculate number of trips for the forecast
Italicized variables are based on the CEC TEDF

## Slide 5: Tailpipe Emissions: Mapping LDVs
Source: CARB analysis of MY2018 Vehicles
 | 1A | 2A | 3A | 4A | 5A | 6A | …
LDA | 100% | 100% | 94% | 86% | 100% | 58% | 
LDT1 | 0% | 0% | 0% | 0% | 0% | 37% | 
LDT2 | 0% | 0% | 6% | 14% | 0% | 5% | 
MDV | 0% | 0% | 0% | 0% | 0% | 0% | 
Mapping was done by class, fuel, and vintage
CEC forecast uses more vehicle classifications than EMFAC
To simplify, we performed a one-to-one class mapping
Mapped based on class definitions and CARB analysis of MY2018 vehicles
Source: CEC analysis
CEC Class_ID | CEC Class | EMFAC 2017 Class
1A | Car-Subcompact | LDA
2A | Car-Compact | LDA
3A | Car-Midsize | LDA
4A | Car-Large | LDA
5A | Car-Sport | LDA
6A | Cross/Ut-Small-Car | LDA
7A | Cross/Ut-Small-Trk | LDT1
8A | Cross/Ut-Midsize | LDT2
9A | Sport/Ut-Compact | MDV
10A | Sport/Ut-Midsize | MDV
11A | Sport/Ut-Large | MDV
11B | Sport/Ut-Heavy(8,500-10,000) | LHD1
12A | Van-Compact | LDT2
13A | Van-Std | MDV
13B | Van-Heavy(8,500-10,000) | LHD1
14A | Pickup-Compact | LDT2
15A | Pickup-Std | MDV
15B | Pickup-Heavy(8,500-10,000) | LHD1

## Slide 6: Tailpipe Emissions: Mapping MD-HD Vehicles
Source: CEC analysis
CEC Class | EMFAC Class
…. | 
GVWR6 | T6 Ag
GVWR6 | T6 CAIRP small
GVWR6 | T6 instate construction small
GVWR6 | T6 instate small
GVWR6 | T6 OOS small
GVWR6 | T6 Public
GVWR6 | T6 utility
GVWR6 | T6TS
…. | 
Based on CEC and EMFAC class definitions
CEC classes map to more than one EMFAC class
Allocated CEC stock by class, fuel, and vintage according to the percent of stock in each EMFAC class

## Slide 7: Tailpipe Emissions: Trips Adjustment
Trips are used to calculate engine start emissions
Because CEC VMT differs from EMFAC VMT, it can be inferred that the trips would also differ
LD Vehicles
  Adjusted trips per vehicle by applying a ratio of CEC VMT per vehicle to EMFAC VMT per vehicle
MD-HD Vehicles
  For 2020 we are adjusting trips similar to LDVs
  For 2021, EMFAC may use CA-VIUS for VMT which is consistent with the CEC MD-HD models. Therefore, VMT per vehicle will align and the adjustment will no longer be required

## Slide 8: Grid Emissions (from Charging PEVs)
Source: CEC Supply Analysis Office
HOURS
Month
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
1 | 0.186 | 0.195 | 0.199 | 0.200 | 0.197 | 0.186 | 0.169 | 0.162 | 0.127 | 0.079 | 0.064 | 0.060 | 0.059 | 0.064 | 0.073 | 0.135 | 0.166 | 0.145 | 0.141 | 0.146 | 0.153 | 0.162 | 0.174 | 0.181
2 | 0.159 | 0.166 | 0.172 | 0.172 | 0.168 | 0.156 | 0.142 | 0.136 | 0.080 | 0.050 | 0.043 | 0.041 | 0.041 | 0.042 | 0.046 | 0.070 | 0.140 | 0.130 | 0.119 | 0.122 | 0.129 | 0.136 | 0.147 | 0.153
3 | 0.138 | 0.145 | 0.148 | 0.146 | 0.139 | 0.124 | 0.117 | 0.120 | 0.073 | 0.045 | 0.040 | 0.039 | 0.039 | 0.039 | 0.040 | 0.043 | 0.080 | 0.110 | 0.097 | 0.101 | 0.106 | 0.117 | 0.126 | 0.133
4 | 0.104 | 0.108 | 0.110 | 0.108 | 0.099 | 0.092 | 0.089 | 0.083 | 0.047 | 0.039 | 0.036 | 0.036 | 0.036 | 0.036 | 0.037 | 0.038 | 0.047 | 0.074 | 0.068 | 0.081 | 0.080 | 0.082 | 0.090 | 0.098
5 | 0.088 | 0.093 | 0.095 | 0.093 | 0.088 | 0.084 | 0.081 | 0.067 | 0.042 | 0.037 | 0.036 | 0.036 | 0.036 | 0.036 | 0.035 | 0.038 | 0.045 | 0.055 | 0.058 | 0.084 | 0.085 | 0.076 | 0.077 | 0.084
6 | 0.094 | 0.101 | 0.105 | 0.107 | 0.106 | 0.101 | 0.090 | 0.064 | 0.045 | 0.039 | 0.038 | 0.037 | 0.037 | 0.037 | 0.038 | 0.041 | 0.046 | 0.057 | 0.065 | 0.087 | 0.101 | 0.088 | 0.088 | 0.095
7 | 0.161 | 0.168 | 0.173 | 0.174 | 0.172 | 0.169 | 0.160 | 0.139 | 0.089 | 0.070 | 0.066 | 0.064 | 0.064 | 0.065 | 0.071 | 0.084 | 0.098 | 0.105 | 0.115 | 0.132 | 0.140 | 0.146 | 0.153 | 0.159
8 | 0.210 | 0.219 | 0.224 | 0.226 | 0.221 | 0.213 | 0.207 | 0.188 | 0.102 | 0.076 | 0.070 | 0.069 | 0.070 | 0.072 | 0.079 | 0.095 | 0.123 | 0.128 | 0.134 | 0.147 | 0.155 | 0.165 | 0.186 | 0.199
9 | 0.217 | 0.226 | 0.229 | 0.228 | 0.222 | 0.211 | 0.207 | 0.202 | 0.118 | 0.079 | 0.072 | 0.069 | 0.069 | 0.071 | 0.081 | 0.107 | 0.141 | 0.141 | 0.147 | 0.160 | 0.174 | 0.188 | 0.199 | 0.208
10 | 0.208 | 0.215 | 0.217 | 0.217 | 0.210 | 0.198 | 0.189 | 0.190 | 0.122 | 0.069 | 0.057 | 0.054 | 0.054 | 0.056 | 0.062 | 0.094 | 0.141 | 0.133 | 0.141 | 0.152 | 0.165 | 0.180 | 0.189 | 0.199
11 | 0.198 | 0.204 | 0.208 | 0.207 | 0.205 | 0.196 | 0.182 | 0.169 | 0.096 | 0.065 | 0.058 | 0.056 | 0.057 | 0.062 | 0.079 | 0.143 | 0.163 | 0.144 | 0.147 | 0.154 | 0.161 | 0.170 | 0.182 | 0.189
12 | 0.211 | 0.218 | 0.222 | 0.223 | 0.221 | 0.213 | 0.198 | 0.188 | 0.136 | 0.088 | 0.075 | 0.071 | 0.071 | 0.078 | 0.094 | 0.167 | 0.179 | 0.159 | 0.159 | 0.163 | 0.171 | 0.180 | 0.193 | 0.202
Mid-Case 2030 Average Grid Emission Intensity Factors
  (Metric Tons CO2/ MWh)

## Slide 9: Discussion Questions
Which GHG and criteria pollutants should we quantify?
  Should we calculate CO2 emissions? Or CO2e emissions (which include CH4 and N2O)?
    Note that grid emissions only account for CO2
  Is it useful to know the annual NOx or other criteria pollutant emissions associated with the forecast?

## Slide 10: Closing
Acknowledgements
  CARB EMFAC team
  Angela Tanghetti, CEC Supply Analysis Office
  Alex Lonsdale for completing the mapping
  Bob McBride for assisting with the MD-HD mapping and other assumptions
  Jesse Gage, Mark Palmere, and Aniss Bahreinian for assisting with the LDV mapping
  Elena Giyenko for her initial work
Questions?
Heidi.Javanbakht@energy.ca.gov